| Project Name: Detention Basin Retrofit of Detention Basin MDB-0054 |
| --- |
| Location: Johanna Farms Road and Castleton Lane in Raritan Township | Subwatershed Priority: Medium |
| BMP Type and Description: Bioretention Basin |
| Issues and Concerns: Residential neighborhoods can be a source of sediment, phosphorus and bacteria for a local waterway. All the surfaces of a residential neighborhood (streets, sidewalks, roofs and lawns) are potential sources of one or more of the pollutants stated above. Pollutants accumulate on roofs, sidewalks and streets. Local wildlife and domestic pet waste can be sources of bacteria and nutrients. The fertilizer used on residential lawns can be a source of phosphorus and nitrogen. These accumulated pollutants can be carried to the local waterways via stormwater runoff. |
| Existing Conditions: Detention Basin MDB – 0054 has an estimated drainage area of 14.3 acres. The drainage area is comprised of a low density residential area. The detention basin is approximately 0.81 acres in size. It has one inlet that connects to a low flow concrete channel. The accumulation of sediment in the concrete low flow channel suggests that it is not maintained on any regular basis. The basin is approximately three to five feet deep with a side slope of 2 to 5%. The detention basin does not have a water quality outlet structure. The outlet is protected by a trash rack. The detention basin is in clear view of a commonly used roadway that is near a residential neighborhood. |
| Proposed Solutions: The solution for this project is in three parts. The first part is re-vegetating the basin. Clusters of turf grass will be replaced with native warm season grasses, herbaceous plants, sedges, ferns and a minimum of woody vegetation. Overtime, the new vegetation will expand past the boundaries of the clusters to cover the entire basin. The new vegetation will increase the infiltration rate of the basin. The basin will not be mowed on a weekly basis as it is now. The vegetation will be allowed to grow tall and increase its ability to filter nutrients and sediment from stormwater runoff. The tall vegetation will have a deeper and more complex root structure allowing the basin to infiltrate greater amounts of water during each storm event. Rerouting the flow of the runoff is the second part of this solution. Currently, the low flow concrete channel directly connects to the outlet and inlet of the basin. The outlet and inlet are very close to each other. The runoff only has to travel 71 feet from the inlet to the outlet. If a section of the low flow concrete channel could be removed, then the water would have to travel much more than 71 feet to exit the basin, allowing more time for sediment and nutrients to be filtered out of the water column. The third part of the solution is a small berm or series of berms that surround the outlet of the basin. The berm would only be about one foot high. The berm would be composed of a permeable material (such as coconut fiber logs or ¾ inch clean stone secured with fabric). The purpose of the berm is to increase the amount of time runoff remains in the basin. The berm would constrict the flow of runoff for small but frequent storms while not interfering with how the basin prevents flooding from larger storms because the runoff would flow over the berm. The berm would give the runoff from smaller storms the opportunity to inundate a larger surface area, providing for a greater opportunity for infiltration and treatment of the runoff. |
| Anticipated Benefits: The detention basin will be expected to infiltrate a greater amount of water during each storm event and remove more nutrients and sediment from the runoff of each storm. The new native vegetation will be allowed to grow tall. The larger vegetation will have a strong filtration effect on the stormwater runoff by removing sediment and nutrients. The larger vegetation will have a larger root structure underground. The root structure will make the soil at the bottom of the basin more porous and increase the infiltration rate. The increased infiltration rate of the basin will allow less water to leave the basin after each storm which would prevent sediment and nutrients from the entering the local water way. After the retrofits are complete, the basin would be very similar to a bioretention basin and is expected to have the same pollutant removal rates. Bioretention basins typically remove 90% of TSS, 60% of total phosphorus and 30% total nitrogen. The removal rates for bioretention basins and wetlands are at or above 90% for fecal coliform (Rusciano, 2007 and Karathanasis et al., 2003). Based upon aerial loading calculations for the drainage area of 100 pounds of total suspended solids/acre/year, 0.6 pounds of total phosphorus/acre/year, and 5.0 pounds of total nitrogen/acre/year, this project would reduce TSS by 1,287 pounds/year, total phosphorus by 5.1 pounds/year, and total nitrogen by 21.5 pounds/year. |
| Major Implementation Issues: There two impediments to the implementation of this project. The first would be permitting. This project requires a permit from the local conservation district. The local soil conservation district would have to sign off on altering the basin. The soil conservation district could be a partner on this project but they would need to be shown some evidence that the berms planned for this project would not adversely affect how the basin prevents flooding downstream or reduce the storage capacity of the basin. The second impediment is aesthetics. This site runs along a commonly used road and is easily visible from the road. The local residents may resist the project because they may prefer the look of the basin with mowed turf grass and landscaped shrubs over a more natural look that is proposed in this project. |
| Possible Funding Sources: 319(h) grants from the New Jersey Department of Environmental Protection |
| Possible Partners/Stakeholders: North Jersey RC&D Raritan Township Hunterdon County Soil Conservation District |
| Task | Task Description | Estimated Cost |
| 1 | Apply for Soil Erosion and Sediment Control Permit | $500 |
| 2 | Complete Topographic Survey and soils test | $1,000 |
| 3 | Prepare Final Design | $2,000 |
| 4 | Prepare Maintenance Plan | $500 |
| 5 | Prepare construction Documents and Solicit Quotes from contractors | $1,000 |
|  | Activities for BMP installation | Unit Costs | Quantity |  |
|  | Remove old and install new vegetation (assumes volunteer work) | $0.25/sq. ft. | 35,283 sq. ft. | $8,820 |
|  | Supervision of Volunteers | $2,000 | 1 | $2,000 |
|  | Install berms | $5,000 | 1 | $5,000 |
|  | Contingency (20%) | $3,164 | 1 | $3,164 |
|  | Total BMP installation costs | $18,984 |
| Estimated Total project cost | $23,984 |
| Annual operation and maintenance cost | $500 |
| Supplemental maps. Graph and photos: A concept design of the site and a design detail of the berm. |