| Project Name: Shoprite Parking Lot Rain Garden |
| --- |
| Location: 272 U.S. 202 Flemington, NJ 08822-1796 | Subwatershed Priority: High |
| BMP Type and Description: Rain Garden |
| Issues and Concerns: Parking lots are considered potential sources of nutrients and sediment in a watershed. Pollutants accumulate on streets (sediment, phosphorus, nitrogen and bacteria). These pollutants are deposited on the surface of the parking lot from wildlife (nutrients and bacteria), vehicle wear and tear (sediment), erosion and wind (sediment and nutrients) and atmospheric deposition (sediment and nutrients). These accumulated pollutants can be carried to local waterways via stormwater runoff. |
| Existing Conditions: This site is part of a parking lot for a strip mall on U.S. Route 202 in Flemington, New Jersey. This portion of the commercial parking lot slopes towards a concrete channel and routes water to a catch basin on Route 202. The drainage area for the concrete channel is approximately 0.18 acres. The concrete channel is surrounded by decorative vegetation that offers no storage options for stormwater runoff, and it is directly underneath the roadside Shoprite sign for the strip mall. The catch basin that collects runoff from the site also collects runoff from U.S. Route 202. |
| Proposed Solutions: The entire drainage area for this project is a parking lot. Parking lots produce runoff during each storm because there is no opportunity for rainfall to infiltrate. By replacing the concrete channel and decorative vegetation around the channel with a rain garden, the runoff from the parking lot will have an opportunity to infiltrate into the ground and reduce the amount of runoff generated from the site for each storm. The concrete channel would be completely removed, and the decorative vegetationwould be removed to install a rain garden. The rain garden would be designed to capture the 1.25 inch storm, otherwise known was the New Jersey Stormwater Quality Storm. The vegetation for the rain garden would have to be carefully chosen and designed. This landscape feature is one of the first things customers see before they enter the strip mall and it would need to have the same or greater appeal than the existing landscaping. The outlet of the rain garden will discharge to the catch basin. During storms runoff will pass through the rain garden and be treated by the vegetation in the rain garden before it is ultimately discharged to the Neshanic River. This will reduce pollutant loading from the site. |
| Anticipated Benefits: Since 90% of the rainfall events deliver less than 1.25 inches of rain, the rain garden is expected to capture approximately 90% of the stormwater runoff from the drainage area that it was designed to treat. By capturing and infiltrating runoff from approximately 90% of all the storms during the course of a year, the rain garden will reduce pollutant loads entering the stream by 90%. By installing a rain garden at this site that capture runoff from the 0.18 drainage area, this project would reduce total suspended solids by 32.4 pounds/year, total phosphorus by 0.15 pounds/year and total nitrogen by 3.6 pounds/year. Additionally, the rain garden will capture, treat and infiltrate approximately 200,000 gallons of stormwater runoff per year. |
| Major Implementation Issues: The one serious obstacle to implementing individual rain gardens is the property owner. The property owner has to first agree to have the rain garden installed on their property. The property owner also has to agree to keep the rain garden for a long period of time and to properly maintain the rain garden for the entire time. If the rain garden is not maintained, the rain garden will not work properly. This problem can be overcome by involving the property owner in the design process as much as possible and by incorporating their ideas as much as possible. |
| Possible Funding Sources: 319(h) grants from the New Jersey Department of Environmental Protection |
| Possible Partners/Stakeholders: North Jersey RC&D Flemington Township Hunterdon County Soil Conservation District |
| Task | Task Description | Estimated Cost |
| 1 | Complete topographic survey and soils test | $500 |
| 2 | Prepare final design | $1,000 |
|  | Activities for BMP installation | Unit Costs | Quantity |  |
|  | Install rain garden (assuming most work completed by volunteers) | $5,000 | 1 | $5,000 |
|  | Supervision of volunteers | $1,000 | 1 | $1,000 |
|  | Contingency (20%) | $200 | 1 | $1,400 |
|  | Total BMP installation costs | $8,400 |
| Estimated total project cost | $14,900 |
| Annual operation and maintenance cost | $100 |
| Supplemental maps, graphs and photos: A concept design of the site and location map. |