| Project Name: Individual Residential Rain Garden |
| --- |
| Location: The residence at 1 Robin Hill Way, Flemington, NJ | Subwatershed Priority: High |
| BMP Type and Description: Rain Garden |
| Issues and Concerns: Roofs and lawns in residential neighborhoods are considered potential sources of nutrients and sediment in a watershed. Pollutants accumulate on streets (sediment, phosphorus, nitrogen and bacteria). The fertilizer used in residential neighborhoods can be a source of phosphorus and nitrogen. Waste from house pets and wildlife found on homeowners properties can be a source of fecal coliform in a watershed. These accumulated pollutants can be carried to local waterways via stormwater runoff. |
| Existing Conditions: The house at 1 Robin Way, Flemington, New Jersey is similar to the rest of the houses in its development. It is a new home built within the last few years. Each house is on a lot of at least 1.25 acres in size. Each lot has some landscaping features with trees and shrubs but the development is relatively new and the vegetative features are small. The large majority of each lot is covered with turf grass. The property is sloped towards the driveway and street. During a storm event, the stormwater runoff carries pollutants from the lawn, roof and driveway to the local waterway. While this individual lot is most likely a small source of pollutant loading, if all the loads from all the houses in the watershed are summed, the source of pollutant loading from residential housing throughout the watershed could be substantial. Additionally, the impervious surfaces associated with residential development increase the volume of stormwater runoff that flows directly into the stream. These increases in runoff volume create a flashy hydrology in the stream, causing stream bank erosion and channel scouring. |
| Proposed Solutions: A rain garden could be used to capture, treat and infiltrate the stormwater runoff from residential development that would ordinarily flow directly to the storm sewer system and the local stream. To capture runoff from the driveway, a small notch will be cut out of the bottom of the driveway. In this notch, a drain will be installed with a grate on top of it. The drain will collect the runoff from the driveway and discharge it to a rain garden just west of the driveway. The rain garden will be large enough to capture all the runoff from the New Jersey Stormwater Quality Storm (1.25 inches). The rain garden will have an outlet for larger storms that discharges the excess runoff onto the street to be routed to a detention basin. The rain garden will be between six inches to 12 inches deep and contain native plants and shrubs. |
| Anticipated Benefits: Since 90% of the rainfall events deliver less than 1.25 inches of rain, the rain garden is expected to capture approximately 90% of the stormwater runoff from the drainage area that it was designed to treat. By capturing and infiltrating runoff from approximately 90% of all the storms during the course of a year, the rain garden will reduce pollutant loads entering the stream by 90%. By installing a rain garden at this site that capture runoff from 1,000 square feet of driveway, this project would reduce total suspended solids by 2.1 pounds/year, total phosphorus by 0.012 pounds/year and total nitrogen by 0.10 pounds/year. Additionally, the rain garden will capture, treat and infiltrate approximately 25,000 gallons of stormwater runoff per year. |
| Major Implementation Issues: The one serious obstacle to implementing individual rain gardens is the property owner. The property owner has to first agree to have the rain garden installed on their property. The property owner also has to agree to keep the rain garden for a long period of time and to properly maintain the rain garden for the entire time. If the rain garden is not maintained the rain garden will not work properly. This problem can be overcome by involving the property owner in the design process as much as possible and incorporating their ideas as much as possible. |
| Possible Funding Sources: 319(h) grants from the New Jersey Department of Environmental Protection |
| Possible Partners/Stakeholders: North Jersey RC&D Flemington Township Hunterdon County Soil Conservation District |
| Task | Task Description | Estimated Cost |
| 1 | Complete topographic survey and soils test | $500 |
| 2 | Prepare final design | $500 |
|  | Activities for BMP installation | Unit Costs | Quantity |  |
|  | Install rain garden (assuming most work completed by volunteers) | $1,000 | 1 | $1,000 |
|  | Supervision of volunteers | $500 | 1 | $500 |
|  | Contingency (20%) | $150 | 1 | $150 |
|  | Total BMP installation costs | $1,650 |
| Estimate total project cost | $2,650 |
| Annual operation and maintenance cost | $100 |
| Supplemental maps, graphs and photos: A concept design of the site and location map. |